LOYOLA COLLEGE (AUTONOMOUS), CHENNAI – 600 034

B.Sc.  DEGREE EXAMINATION –COMPUTER SCIENCE

FOURTH SEMESTER – APRIL 2007

CS 4500 - MICROPROCESSORS & COMPUTER ARCHITECHTURE

Date & Time: 21/04/2007 / 9:00 - 12:00	     Dept. No. 	Max. : 100 Marks

Part – A

Answer ALL questions.								            10 x 2 = 20

- Draw a block diagram of programmable registers in 8085.

- List all the flags related with arithmetic and logic unit.

- What is an assembler?

- List out the data formats in 8085.

- Specify the number of times the following loops are executed.

LXI B, 0007H

LOOP:   DCX B

MOV A, B

ORA C

JNZ LOOP

- Find out the number of times the following loops are executed.

MVI A, 17H

LOOP:   ORA A

RRC

JNC LOOP

- Define executive address.

- Draw the basic symbols of Register Transfer Language.

- Define Instruction Code.

- What are the basic registers in a basic Computer?

Part – B

Answer ALL questions.							    		5 x 8 = 40

- a) With neat diagrams, explain 8085 microprocessor architecture. (Or)

b) Explain All the functional units of a microcomputer system in detail.

- a) Classify 8085 instruction set by their word size. (Or)

b) Explain Branch Instructions of 8085 instruction set.

- a) Write an assembly language program to

  - Clear Accumulator

  - Add 47H

  - Subtract 92H

  - Display the result after doing the above operation.  (Or)

b) Write an assembly language program to multiply two numbers.

- a) Explain 4 bit binary incrementer circuit with diagrams (Or)

b) Explain logic micro operations with suitable symbolic descriptions.

- a) Implement common bus for all the basic registers in a microcomputer. (Or)

b) With neat diagrams, explain one stage of adder and logic circuit.

Part – C

Answer ANY TWO questions.	 					   	            2 x 20 = 40

- a) Explain various addressing modes of a microcomputer. (10)

b) How do you classify the memory for 8085 Microprocessor? Explain. (10)

- a) Explain various interfacing devices in a microcomputer with neat diagrams. (10)

b) Write complete guidelines for writing an assembly language programs. (10)

- a) Explain Register Transfer Language for Logic Micro operations. (10)

b) Explain Memory Reference Instructions with suitable symbolic descriptions. (10)

*******

# Text boxes

HC 09