LOYOLA COLLEGE (AUTONOMOUS), CHENNAI – 600 034

M.Sc. DEGREE EXAMINATION – PHYSICS

FIRST SEMESTER – NOV 2006

# PH 1808 - ELECTRONICS - I

Date & Time : 31-10-2006/1.00-4.00 	Dept. No. 	Max. : 100 Marks

PART – A

- Draw the circuit diagram of an Integrator using an operational amplifier.

- State any two advantages of a R-2R D/A converter over a binary weighted D/A converter.

- Develop an ASM program for µP 8085 which sets the C register to 1 if the MSB or LSB of the number at memory location 8100h is '1' else sets C register to 0.

- Develop a subroutine for µP 8085 to find the factorial of the number passed to it through the B register.

- Develop a program for µP 8085 to convert a two digit packed BCD number in register A to unpacked BCD format in BC register pair.

- Develop a program for µP 8085 to generate a square wave in SOD line.

- Develop a program segment for µP 8085 to mask RST5.5 and enable the rest.

- Write notes on the ALE and READY lines of µP 8085.

- State the advantage of relative branching available in Z80 over absolute branching.

- Develop an ASM program for µP Z80 to input 40 bytes from I/O port 30h and to store them from 8100h using string primitives.

PART – B

- Sketch neat circuit diagrams of Op-amp based inverting and non-inverting amplifiers. Also derive expressions for their voltage gains.				(6+6.5)

- With timing diagram, explain the instruction cycle for LXI H,FFFFH of µP 8085.

- If the crystal frequency of an 8085 system is 1 M.Hz, calculate the delay generated by the following segment of code.

MVI A,50H

rpt: 	DCR A

JNZ rpt

- Write notes on the software and hardware interrupts available in µP 8085.

- Explain the various block transfer and block search instructions available in µP Z80.

PART – C

- Develop an interface and program for µP 8085 to implement an 8 bits successive approximation A/D converter.

- Develop a program for µP 8085 to solve n1Cr1 - n2Cr2 . Use a subroutine for factorial.

- There are eight LEDs and two switches (S0 and S1) connected to ports, PA and PB respectively. Develop an ASM program for (P 8085 to generate the following pattern.

| S1 | S0 | LEDs |
| --- | --- | --- |
| 0 | 0 | OFF |
| 0 | 1 | Binary Ascending |
| 1 | 0 | Left to Right |
| 1 | 1 | All Blinking |

- Explain memory mapped I/O and I/O mapped I/O schemes of (P8085. Also explain with a neat circuit diagram how I/O mapped I/O scheme can be implemented with address decoding for 2 ROM chips of 8KB each and 6 RAM chips of 8KB each. (6+6.5)

- Develop a program for Z80 to copy the elements of an array into an overlapping array.

# Text boxes

AC 13